## Slide 1: PHX: Memory Speed HPC I/O with NVM
Sudarsun Kannan, Ada Gavrilovska, Karsten Schwan
Pradeep Fernando

## Slide 2: Node Local Persistent I/O ?
Node local checkpoint/ restart
  Recover from transient failures ( node restart)
  Transient/ soft failures – not permanent failures
  More soft failures in future machines
Locally stored analytics output
  Co-running analytics

## Slide 3: NVRAM is Ideal for Persistent I/O
Read/ write latencies comparable to DRAM
  100x faster than SSD
Persistent data writes
  Data retention time is >10 years for Memristor
Denser memory
  Low chip area per bit -> more capacity
Memory device -> load/ store operations

## Slide 4: NVRAM Bandwidth?
HPC applications move data in bulk
  I/O after implicit/explicit synchronization
More I/O in future Exascale simulations
  - More cores per node -> more data
Poor bandwidth scaling of NVRAM
  Device physics
  RAID like structures -> more energy

## Slide 5: Key Idea: Aggregate Bandwidth Checkpoints
NVRAM provides denser persistent memory, but has limited bandwidth
DRAM has superior bandwidth compared to NVRAMs (4x-8x)
Accelerate critical path data movement with bandwidth aggregation
NVRAM
DRAM

## Slide 6: Phoenix (PHX) Design

## Slide 7: Problem : Software Stack Overheads
Using NVRAM as a block device under file system lengthens the I/O path.
Kernel Space
VFS
File system
Generic block device
Device driver
NVRAM
write
read
User space
NVRAM
Mapped memory
map/ brk
Store
Load
User space

## Slide 8: Problem : NVRAM Access Latencies
NVRAM writes/ reads are expensive
  - Writes takes 4x more time than DRAM
  Application works with a DRAM allocated object
NVRAM
DRAM
Application
foo
bar
Object handles/ keys: foo, bar
Checkpoint call
bar
foo
foo:v1
bar:v1

## Slide 9: Resulting PHX C/R API
Allocate checkpoint object
Create a versioned copy and move it to NVRAM

## Slide 10: Problem: Limited NVRAM Bandwidth
Simultaneous bandwidth usage of both NVRAM and DRAM
DRAM Staging Buffer
NVRAM
De-stage
Objects snapshots from application heap
Split the objects to DRAM & NVRAM

## Slide 11: Checkpoint Data Split
Optimal data split ratio is same as the device bandwidth ration
Prioritize staging for late access variables – immune to optimizations (e.g. Pre-copy)
Memory budget allocated for staging.

## Slide 12: Fault Tolerance of Staged Data

## Slide 13: Staging Buffer Data Loss
Staged data is vulnerable to transient node failures.
Node restart
NVRAM
DRAM Staging Buffer
De-stage
Persistent data loss

## Slide 14: Buddy Node Replication (N=2)
Node restart
DRAM staging buffer
Replicate and de-stage
Buddy node
Consistent restart state using buddy replica of staging buffer
DRAM
NVRAM

## Slide 15: Failure Probability of Staged Data
N=2, buddy replication scheme brings down the staged data loss probability to negligible level.

## Slide 16: Energy Cost Analysis

## Slide 17: Energy Overheads of PHX
PHX energy overheads
  - Checkpoint staging
  Stage buffer replication
Depends on
  Interconnect technology
  Distance to buddy
  DRAM write costs
Energy costs of data staging
Buddy replication
Additional energy costs

## Slide 18: Energy Savings of PHX
Fast PHX checkpoints cut down the total simulation time.
Energy savings!
Execution
time – naive
Execution
time – PHX
Time reduction

## Slide 19: PHX Saves Energy
For DRAM:NVRAM bandwidth ratio of 2:1 PHX can stage up to ~750 MB (total checkpoint size is 1GB) when the buddy node is one switch away
Break even point
Careful selection of PHX configuration parameters will lead to
both fast checkpoints and energy savings.

## Slide 20: Evaluation
Four node cluster run in the stampede supercomputer
Emulated NVRAM using software delays
Three application benchmarks
  GTC
  CM1
  S3D

## Slide 21: GTC Benchmark
Checkpoint data-intensive application
Staging buffer size -- 50% of checkpoint data per interval
Lot of early access variables

## Slide 22: GTC Benchmark
Checkpoint time is 37% compared to compute
2x Improvement
12x
NVRAM bandwidth seen by a core.

## Slide 23: CM1 Benchmark
Compute heavy application
Staging buffer = 50% checkpoint data per interval
No early access variables

## Slide 24: CM1 Benchmark
2x time reduction

## Slide 25: Total Simulation Time
Application – GTC
Total time over 10 compute iterations
18% improvement

## Slide 26: Summary
PHX – a bandwidth aware checkpoint/ restart scheme for NVM
  Reduce C/R time , accelerate simulation time
  Reduce energy requirements
The technique shows promising results in the evaluated scale
  C/R costs will only increase with scale, so solutions like PHX will only gain importance
Future work
  Evaluate against analytics workloads
  Deployment and evaluation at scale
  Will be carried out as part of the UNITY SSIO/ SICM ECP projects, funder by US DoE

## Slide 27: Thanks!
Pradeep Fernando
pradeepfn@gatech.edu
Sudarsun Kannan, Ada Gavrilovska, Karsten Schwan
We thank IEEE TCPP and the National Science Foundation for providing travel support to attend IEEE HiPC 2016
Q&A